## Slide 1
Objective
Understand how microbial reduction of Hg(II) species and dissolved natural organic matter (DOM) in anoxic environments are coupled.
New Science
DOM plays a dual role in Hg chemistry: it reduces Hg(II) to Hg(0) but it also strongly complexes Hg, thereby affecting Hg(0) production.
Ligand-induced oxidative complexation of Hg(0) with DOM exerts a significant control on Hg(0) oxidation and sequestration in anoxic environments.
Significance
The redox state of sulfur in DOM and the DOM:Hg ratio critically influence the transformation of Hg and thereby, the potential microbial production of toxic methylmercury (CH3Hg+).
Dual Role for Organic Matter in Mercury Cycling
Gu B., Y, Bian, C. L. Miller, W. Dong, X. Jiang, and L. Liang. 2011. Proc. Natl. Acad. Sci. USA. 108, (in press).
Department of Energy • Office of Science • Biological and Environmental Research
1 BER Overview
Depending on the sulfur redox state:
2R–SH + Hg(0) R–S–Hg(II)–S–R + 2H+ + 2e-
or
R–S–S–R’ + Hg(0) R–S–Hg(II)–S–R’
Hg(II) reduced (%)
Humics in solution (mg/L)
Initial Hg(II)=10 nM
Notes: An examination of the interactions between Hg and DOM in anoxic environments. This work was published in Proceedings of the National Academy of Sciences in January 2011.
Note for the first point under new science: the balance of these two reactions result in the observation that at low DOM, Hg(0) increases with DOM, but beyond the DOM concentration at which Hg(0) reaches peak production, Hg(0) decreases with DOM.